Plan/Constructability/Biddability Review

SMALL LPA PROJECTS

Sidewalks, Sign Replacements, Guardrail, Pavement Markings

Bike paths, Pedestrian Signals, Landscaping, Building Renovations

PLAN / CONSTRUCTABILITY / BIDDABILITY REVIEW

Purpose and Instructions

NOTE: Any projects that involves the majority of the work on the roadway surface or base, or bridge must use the large project form

Project types: Sidewalks, Bicycle Paths, Landscaping, Building Renovations, Pavement Markings, Sign Replacements, Guardrails

Purpose:

- To provide information to assist in producing quality plans.

- To provide a history of information that is easily accessible.

- To provide questions to stimulate discussion of potentially problematic areas.

- To provide questions to stimulate checking details and items required to complete the project.

- To provide aid during design for QA/QC

- To provide primary discussion for the plan-in-hand meeting

Instructions for completing the form

      - The form shall be completed by the designer and checked by the reviewer at both 100% preliminary plans and final plans.

- The form may be filled out by any district person (ADA, Area Engineer, Lab Engineer, etc.) but the District Project Coordinator must sign the signature sheet that he concurs with the comments.  It is encouraged that the Area Engineer and the District Project Coordinator both review the plans.

- Most questions are designed that a “NO” answer will require comments on what is missing or needed.

- Most questions are designed that a “YES” answer means the plans meet the project needs or a follow up question is required.

- Comments are to be written at the back of the form along with reference numbers for the plan section and checklist item number for easy reference. (Example III-2)

- The Final Plan / Biddability submittal shall have copies of the completed PIH review attached (if applicable). If missing contact the Project Manager for a copy. The plans and specifications should provide the details and pay items to bid the project.

- Designers and reviewers will ensure all comments are addressed.

- Each review is considered complete when all comments are addressed

- If a question is answered N/A, the question is not applicable to project.

- Final Plan reviews (ACP) shall have the completed 95% Preliminary Plan (PIH) review (if applicable) attached.  It may be helpful to reference the PIH plan set during the ACP review.

Applicable Section for Review

| State Project No. |  | Route No. |  |  |  | Preliminary Plans |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| F.A.P. No. |  | Parish |  |  |  | Final Plans |  |  |
| Project Name: |  |  |  | Constructability/Biddability |  |  |  |  |  |

PLAN-IN-HAND INSPECTION REPORT

AND

CONSTRUCTABILITY / BIDDABILITY REVIEW

| Description |  | 100% Prelim Designer | 100% Prelim Reviewer | Final Plans Designer | Final Plans Reviewer | Construction PS&E Biddability |
| --- | --- | --- | --- | --- | --- | --- |
|  | N/A | Y | N | Y | N | Y | N | Y | N | Y | N |
| TITLE SHEET |  |  |  |  |  |  |  |  |  |  |  |
| Is most of the work off of the roadway surface/ base or a bridge? (If no, use the large project forms) |  |  |  |  |  |  |  |  |  |  |  |
| Does the project name on the title sheet and plan sheets match the name in the Project System? |  |  |  |  |  |  |  |  |  |  |  |
| For multiple projects, are all project numbers shown? |  |  |  |  |  |  |  |  |  |  |  |
| Is the type of construction correct? |  |  |  |  |  |  |  |  |  |  |  |
| Is the Project Length Table correct? |  |  |  |  |  |  |  |  |  |  |  |
| Are the C.S. Log miles (state route) correct? |  |  |  |  |  |  |  |  |  |  |  |
| Are the arrows on the Layout Map pointing to the correct location? |  |  |  |  |  |  |  |  |  |  |  |
| Are the project limits, (beginning, ending) equation, exceptions (RR, Bridge, etc.) and other callouts shown on the Layout Map and match the same callouts on the plan and summary sheets? |  |  |  |  |  |  |  |  |  |  |  |
| Is the north arrow shown on the Layout Map? |  |  |  |  |  |  |  |  |  |  |  |
| Is the scale for the Layout Map labeled correctly? |  |  |  |  |  |  |  |  |  |  |  |
| Is the sheet count correct? |  |  |  |  |  |  |  |  |  |  |  |
| Are all applicable standard plans noted? |  |  |  |  |  |  |  |  |  |  |  |
| Are the latest versions of Standard Plans and Special Details used? |  |  |  |  |  |  |  |  |  |  |  |
| Are design exceptions shown on title sheet and can they be located in ProjectWise? |  |  |  |  |  |  |  |  |  |  |  |
| Is the traffic data current and does it reflect actual conditions? |  |  |  |  |  |  |  |  |  |  |  |
| I. TYPICAL SECTION SHEETS |  |  |  |  |  |  |  |  |  |  |  |
| Is the existing typical section shown? |  |  |  |  |  |  |  |  |  |  |  |
| Are project limits covered by typical sections? |  |  |  |  |  |  |  |  |  |  |  |
| Have sequential typical sections been provided, if necessary? |  |  |  |  |  |  |  |  |  |  |  |
| Does the typical section fit within existing and/or proposed right-of-way? (Check cross sections) |  |  |  |  |  |  |  |  |  |  |  |
| Are all measurements, thicknesses, and slope rates labeled and accurately indicate what is to be constructed? |  |  |  |  |  |  |  |  |  |  |  |
| Is the typical section compliant with ADA? |  |  |  |  |  |  |  |  |  |  |  |
| Are striping and new lane widths shown? |  |  |  |  |  |  |  |  |  |  |  |
| Will project drain properly during construction? |  |  |  |  |  |  |  |  |  |  |  |
| Are Design Exceptions required/noted? |  |  |  |  |  |  |  |  |  |  |  |
| Are all station ranges accounted for and match the limits shown on Title Sheet and Plan/Profile sheets? |  |  |  |  |  |  |  |  |  |  |  |
| Are all transitions shown? |  |  |  |  |  |  |  |  |  |  |  |
| Is the minimum ditch elevation dimension shown on the typical section? |  |  |  |  |  |  |  |  |  |  |  |
| Are the limits of seeding and fertilizer shown? |  |  |  |  |  |  |  |  |  |  |  |
| Are typical sections provided for ancillary items with appropriate pay items? |  |  |  |  |  |  |  |  |  |  |  |
| II. SUMMARY SHEETS |  |  |  |  |  |  |  |  |  |  |  |
| Are all pay items in the plans shown on the summary sheets? |  |  |  |  |  |  |  |  |  |  |  |
| Will existing ditch cleaning be required? |  |  |  |  |  |  |  |  |  |  |  |
| 2a. If yes, are there limits and pay items? |  |  |  |  |  |  |  |  |  |  |  |
| Are there sufficient removal items for all of objects being removed? |  |  |  |  |  |  |  |  |  |  |  |
| Is method of payment for earthwork design addressed appropriately? |  |  |  |  |  |  |  |  |  |  |  |
| Have sufficient temporary erosion control items been included? |  |  |  |  |  |  |  |  |  |  |  |
| Is an item for saw cutting included for removal or patching? |  |  |  |  |  |  |  |  |  |  |  |
| Is an item for saw cutting included for removal of concrete drives? |  |  |  |  |  |  |  |  |  |  |  |
| Is a bedding material item included? |  |  |  |  |  |  |  |  |  |  |  |
| Is traffic maintenance aggregate required? |  |  |  |  |  |  |  |  |  |  |  |
| 9a. If yes, how much? |  |  |  |  |  |  |  |  |  |  |  |
| Is there a summary of drainage structure sheet provided? |  |  |  |  |  |  |  |  |  |  |  |
| 10a. If yes, are items adequately covered? |  |  |  |  |  |  |  |  |  |  |  |
| 10b. If no, is one required? Why? |  |  |  |  |  |  |  |  |  |  |  |
| Are work elements identified clearly with all corresponding pay items included with adequate quantities to construct project? (i.e. summary tables) |  |  |  |  |  |  |  |  |  |  |  |
| Is there any work under this project designated as “no direct pay”? |  |  |  |  |  |  |  |  |  |  |  |
| 11a. If yes, is this work clearly linked to a specific pay item that can be quantified in the contractor’s bid item list? |  |  |  |  |  |  |  |  |  |  |  |
| Are permanent erosion and pollution control items included? |  |  |  |  |  |  |  |  |  |  |  |
| Are exceptions shown and properly depicted in tables? (RR, Bridge, etc.) |  |  |  |  |  |  |  |  |  |  |  |
| Has a detailed check of all quantity tabulations (addition and multiplication) been completed? |  |  |  |  |  |  |  |  |  |  |  |
| Has a detailed check of tables matching the plans (typical sections, plan/profiles, cross sections, etc.) been completed? |  |  |  |  |  |  |  |  |  |  |  |
| Has a detailed check of quantity transfers from tables to Master Summary been completed? |  |  |  |  |  |  |  |  |  |  |  |
| Do pay items conform to current “Master Item List/Site Manager”? |  |  |  |  |  |  |  |  |  |  |  |
| Have specialty items been given appropriate numbers compliant with Site Manager and Trns*port? |  |  |  |  |  |  |  |  |  |  |  |
| Were any new NS items created? |  |  |  |  |  |  |  |  |  |  |  |
| 20a. If yes, has information been sent to Contracts and Specifications? |  |  |  |  |  |  |  |  |  |  |  |
| III. PLAN-AND-PROFILE SHEETS |  |  |  |  |  |  |  |  |  |  |  |
| Are the benchmark data, required elevations, and curve data on the plans? |  |  |  |  |  |  |  |  |  |  |  |
| Is all alignment information shown and been checked for accuracy (including horizontal and vertical curve data)? |  |  |  |  |  |  |  |  |  |  |  |
| Has sight distance been checked including vertical and horizontal curves? (landscaping) |  |  |  |  |  |  |  |  |  |  |  |
| Have design exceptions been completed and documented on the plans? |  |  |  |  |  |  |  |  |  |  |  |
| Can design exceptions be located in the project files? |  |  |  |  |  |  |  |  |  |  |  |
| Is there space between the R/W line and drainage structure to allow for utility relocation? |  |  |  |  |  |  |  |  |  |  |  |
| Are all right-of-way ties and property line dimensions shown on plans at all right-of-way breaks, and along curves as appropriate? |  |  |  |  |  |  |  |  |  |  |  |
| 7a. If state route, are right-of-way markers shown at all breaks? |  |  |  |  |  |  |  |  |  |  |  |
| Are limits of construction shown and located within existing or required right-of-way or construction servitude? |  |  |  |  |  |  |  |  |  |  |  |
| Will any right-of-entry agreements be required? |  |  |  |  |  |  |  |  |  |  |  |
| 9a. If yes, is this satisfactory? |  |  |  |  |  |  |  |  |  |  |  |
| 9b. If yes, who will secure it? |  |  |  |  |  |  |  |  |  |  |  |
| Are driveways, sidewalks, turnouts, etc. within the right-of-way (either existing or required) shown? |  |  |  |  |  |  |  |  |  |  |  |
| Are concrete/asphalt removal shown with appropriate patterns, including driveways, sidewalks, parking lots, etc.? |  |  |  |  |  |  |  |  |  |  |  |
| Is all work including driveway types, widths, and stations shown? Are handicapped ramps and items shown? Do they match the tables? |  |  |  |  |  |  |  |  |  |  |  |
| Is the sidewalk clear of obstacles (ADA access)? |  |  |  |  |  |  |  |  |  |  |  |
| Does existing horizontal or vertical clearance allow for construction? |  |  |  |  |  |  |  |  |  |  |  |
| Are all the utility owners with contact numbers listed? |  |  |  |  |  |  |  |  |  |  |  |
| Are the existing utility locations marked in the plans? |  |  |  |  |  |  |  |  |  |  |  |
| Are the utility conflict boxes and their location noted on the plans? |  |  |  |  |  |  |  |  |  |  |  |
| Are there utility conflicts with drainage? |  |  |  |  |  |  |  |  |  |  |  |
| Is there a method to connect new and existing drainage structures? |  |  |  |  |  |  |  |  |  |  |  |
| If new or altered drainage structures are planned, are utility adjustments required? |  |  |  |  |  |  |  |  |  |  |  |
| Are retaining walls required? |  |  |  |  |  |  |  |  |  |  |  |
| 21a. If yes, are details provided for the walls? |  |  |  |  |  |  |  |  |  |  |  |
| Have notes been checked to verify how all work items will be paid? |  |  |  |  |  |  |  |  |  |  |  |
| Are the locations, sizes, and descriptions of drainage structures to be removed shown? |  |  |  |  |  |  |  |  |  |  |  |
| Have construction or drainage servitudes been shown? |  |  |  |  |  |  |  |  |  |  |  |
| Are the limits of clearing, grubbing, and landscaping shown? |  |  |  |  |  |  |  |  |  |  |  |
| Can any significant tree be allowed to remain? |  |  |  |  |  |  |  |  |  |  |  |
| 26a. If yes, are those to remain been identified? |  |  |  |  |  |  |  |  |  |  |  |
| Are there apparent conflicts between plans and specifications? |  |  |  |  |  |  |  |  |  |  |  |
| Do general site conditions conform to those represented in plans? |  |  |  |  |  |  |  |  |  |  |  |
| Is there a note stating existing drainage structures will be removed unless otherwise noted with a table showing amounts of each size pipe to be removed? |  |  |  |  |  |  |  |  |  |  |  |
| Is the north arrow shown with the proper scale? |  |  |  |  |  |  |  |  |  |  |  |
| Do taking lines extend beyond the limits of the project? |  |  |  |  |  |  |  |  |  |  |  |
| Are vertical and horizontal limits of removal clear? |  |  |  |  |  |  |  |  |  |  |  |
| IV. DRAINAGE PLAN-AND-PROFILE INFORMATION |  |  |  |  |  |  |  |  |  |  |  |
| If subsurface drainage is being used, is there any evidence of effluent sewerage entering existing roadside ditches? |  |  |  |  |  |  |  |  |  |  |  |
| 1a. If yes, what is the plan of action |  |  |  |  |  |  |  |  |  |  |  |
| Has sufficient drainage excavation and/or cleaning of outfall lateral required for adequate drainage been shown? |  |  |  |  |  |  |  |  |  |  |  |
| 2a. If yes, who is cleaning laterals (City, Parish)? |  |  |  |  |  |  |  |  |  |  |  |
| Will cleaning be required for existing drainage structures? |  |  |  |  |  |  |  |  |  |  |  |
| 3a. If yes, are pay items included? |  |  |  |  |  |  |  |  |  |  |  |
| Are ditches compatible with existing and proposed drainage structures? |  |  |  |  |  |  |  |  |  |  |  |
| Are design drainage elevations shown in the plan compatible with the existing conditions? |  |  |  |  |  |  |  |  |  |  |  |
| Is there a provision for temporary drainage? |  |  |  |  |  |  |  |  |  |  |  |
| Is there a method to connect new and existing drainage facilities? |  |  |  |  |  |  |  |  |  |  |  |
| VII. SEQUENCE OF CONSTRUCTION |  |  |  |  |  |  |  |  |  |  |  |
| Are traffic operations requirements properly addressed? (i.e., signing, pavement markings signal, etc.) |  |  |  |  |  |  |  |  |  |  |  |
| Is there sufficient clearance within the work zone for the operations (such as crane swing room)? |  |  |  |  |  |  |  |  |  |  |  |
| Have restrictions (e.g. lane closure, general construction or peak-hour restrictions in urban areas) been identified? |  |  |  |  |  |  |  |  |  |  |  |
| Are there notes covering pay for traffic control items? |  |  |  |  |  |  |  |  |  |  |  |
| Scheduling & Phasing |  |  |  |  |  |  |  |  |  |  |  |
| Is scheduling and phasing coordinated with activity needs? (Schools, festivals, harvesting, parallel routes, etc.) |  |  |  |  |  |  |  |  |  |  |  |
| Have requirements for local/state/federal special permits been addressed? |  |  |  |  |  |  |  |  |  |  |  |
| Is safe pedestrian access and access to business and residences provided? |  |  |  |  |  |  |  |  |  |  |  |
| VIII. GENERAL |  |  |  |  |  |  |  |  |  |  |  |
| Is salvageable material shown and designated where to haul it? |  |  |  |  |  |  |  |  |  |  |  |
| Has the maintenance/liability agreement been completed for sidewalks, lighting or bike paths and can be located? |  |  |  |  |  |  |  |  |  |  |  |
| Have any general notes redundant to the specification book been removed? |  |  |  |  |  |  |  |  |  |  |  |
| Are the environmental mitigation items included in the plans? |  |  |  |  |  |  |  |  |  |  |  |
| Is the project’s disturbed area provided in the submittal? |  |  |  |  |  |  |  |  |  |  |  |
| Have conflicts between landscaping and planting requirements with utilities (e.g. irrigation lines) and billboards been resolved? |  |  |  |  |  |  |  |  |  |  |  |
| Is there sufficient space (25’-30’) for power mowers between additional trees that are planted? |  |  |  |  |  |  |  |  |  |  |  |
| General Constructability and Biddability |  |  |  |  |  |  |  |  |  |  |  |
| Are there adequate staging areas for the contractor? |  |  |  |  |  |  |  |  |  |  |  |
| Are all required work items covered under proper pay items? |  |  |  |  |  |  |  |  |  |  |  |
| Is the contract type and time period sufficient? |  |  |  |  |  |  |  |  |  |  |  |

| 100% Preliminary Plans LPA Project Designer |  | Date |
| --- | --- | --- |
| 100% Preliminary Plan LPA Project Reviewer |  | Date |
| Final Plan LPA Project Designer |  | Date |
| Final Plan LPA Project Reviewer |  | Date |
| DOTD Constructability / Biddability Reviewer (DOTD Construction Project Coordinator) |  | Date |
| DOTD Area Engineer |  | Date |
| Local Public Agency Responsible Charge |  | Date |

NOTES PAGE

| Item No | Comment | Response |
| --- | --- | --- |

# Text boxes

The LPA Project Designer or the Engineer of Record is responsible for accuracy and completeness of the plans and related designs prepared for the project. The designer is responsible for the quality of work of each person involved in the efforts to bring the project to production readiness.

The LPA Project Reviewer has not been involved in the design of the project, but is an engineer who detailed checks the design to ensure quality assurance.

The LPA Responsible Charge is responsible for signing the final document submission of this checklist