## Slide 1: LaPave Walkthrough
Asphalt 501/502

## Slide 2: Basics
File is locked down to prevent overwriting of formulas
Light blue cells are for user inputs, some may be drop downs
One file per Lot

## Slide 3: Reporting Tab
[Import Mat Code] – imports SiteManager codes from server or another file
[Check Latest Version] – checks for newer version on the shared location [internal only]
[Upload File to Server] – uploads to shared location on DOTD network [internal only]
[Print]s – can select Y/N on sections to print

## Slide 4: Material Setup Tab
Users select materials typically used in their plant, some values can be completed here, these will populate throughout the file.
Custom name set by user to distinguish if two aggregates from same source.
Options to import/export materials setup too

## Slide 5: JMF Input Tab
[Import] button will import JMF data from another LaPave file of similar type
(includes material setup)

## Slide 6: JMF Input Tab
JMF header info
Mix Type, Use, and Nom Agg Size will set limits for other parts of the application
Project and mix info will be populated to other sheets

## Slide 7: JMF Input Tab
Aggregate entry
Select Aggregate class (this will update aggregate type dropdowns to match materials setup)
Select Aggregate Types (if material setup value are filled, sheet will populate with these)
Aggregate % will be transferred to the aggregate design tab
%Ret No.8 and No.4 are populated from the aggregate design tab
Flags will show if entry does not meet spec for selected mix type

## Slide 8: JMF Input Tab
Enter Asphalt Information
Warm mix and Rap information are here also
Gradations are populated from design and validation

## Slide 9: Comp. Grad. And FAA Input Tab
Aggregate names and % will be transferred here
Values will pull from material setup, but users can manually enter or update gradation.

## Slide 10: Comp. Grad. And FAA Input Tab
The composite gradation will be plotted with the spec limits of the mix type selected on the JMF input tab
Flags show if out of spec

## Slide 11: Comp. Grad. And FAA Input Tab
Ignition oven test entries can be found below the gradation entry
Entry fields will change depending on the oven temperature correction selection

## Slide 12: Optimum AC Test Results Tab
Enter design rice and design brick information

## Slide 13: Optimum AC Test Results Tab
Enter design verification brick information in the section below

## Slide 14: Optimum AC Test Results Tab
Some parameters will be plotted with design data vs. verification data

## Slide 15: Moisture Susceptibility Design Tab
Enter LWT or TSR data for design and verification here

## Slide 16: JMF Check Tab
Summary sheet to check values
A flag checklist is located here that will show any JMF related flags
Signature lines
There is a dropdown to select if JMF parameters are computed off design %air or the verification briq

## Slide 17: JMF Tab
Printable JMF page in DOTD format
Populates from design and validation tabs

## Slide 18: Validation Input Tab
Input for sublots for validation of JMF
Users can select burn oven options, entry fields change depending on selection
Roadway cores can be entered at the bottom

## Slide 19: Validation Tab
Summary for validation inputs
Runs statistics for validation
Flags if parameters are not meeting spec of selected mix type in JMF
show PWL and %pay

## Slide 20: Plant Tabs
Plant acceptance – up to 6 sublots for DOTD submission
Plant report pulls from Plant acceptance
Plant QC – up to 6 sublots for contractor use
Plant Verification up to 3 sublots for DOTD use

## Slide 21: Plant Tabs
Typical plant entry fields
Sublot 6 will activate if tonnage is entered

## Slide 22: Plant Tabs
Entry for LWT and drain down testing below sublots

## Slide 23: Plant Tabs
Lot statistics below
flags will show for items out of spec

## Slide 24: Roadway Tab
Entry for cores by sublot
  up to 4 acceptance
  1 verification
  ML/minor determined by mix use selected
  Gmm pulled from plant acceptance
Entry for Gmm check
  If out of tolerance, flag will show to test remaining

## Slide 25: Roadway Tab
If resolution Gmm is filled, the average resolution Gmm will become the Gmm used for all core calculation for the lot
If resolution cores is filled, the core values will be used to calculate pay

## Slide 26: Roadway Tab
Pay sheet determines count for ML/minor uses
Tonnage summary
All Mainline cores are used for PWL for pay
If ML Resolution cores, resolution cores used for PWL for pay
Average of Minor cores for each sublot is used for pay, then weighted average by tons to determined final pay
If Minor Resolution cores, the core will replace the sublot average for pay
Final pay computed with weighted average by tons