## Slide 1
The Pod
Bill Ische, Business Development Manager Chris Jannace, Detection Specialist 03 September 2015
The Trafficware Pod
As a Means of Collecting Purdue High Resolution Data
The Pod
Engineer Training

## Slide 2: Agenda
Components review
Installation Review
TSI review and planning considerations (Pod placement, spacing, antenna ranges)
Software programming
Intersection Design
  Standard presence detection
  Adaptive requirements
  SPM requirements
ATMS Integration
Reports Available

## Slide 3: Components

## Slide 4: Components Pod Sensor
900 MHz Communication
6’ x 6’ Detection Area
10 Year Battery Life
  700 detections per hour (24/7)

## Slide 5: Components Access Point
120VAC
Wireless (internal) or Wired Communication
3 Radios (external)
Box designed to fit articulating style bracket (comes with Access Point kit)

## Slide 6: Software Programming Access Point
Serial
Number
Comm ID
RF Cable to Antennas
Radio 1
(Omni)
Radio 3
(Panel)
Radio 2
(Panel)
16 awg Cable (Power) to Power Panel (Cabinet)
EIA-485 Cable to Lightning Suppression Panel (Cabinet)

## Slide 7: Components Base Station
ZigBee standard compliant encryption used between Base Station and Access Point
Can communicate effectively with two Access Points
Browser-based GUI (You own the Base Station, You own the GUI)
SDLC or parallel wiring connection to controller / cabinet based on configuration

## Slide 8: Software Programming Base Station
Serial Number (Sticker)
Cable to Laptop
Antenna to top of Cabinet
Cable to Controller
Cable to Switch / Cell Modem
Cable to Expansion Cards (if not SDLC)
Cable to Access Point (thru EIA-485 Lightning Suppression Panel

## Slide 9
Detection Zones Pod Spacing

## Slide 10
TSI Review & Planning Considerations
*** Go to Google Earth to review ranges

## Slide 11
TSI Review & Planning Considerations

## Slide 12
TSI Review & Planning Considerations
Antennas
AP Placement
Which Radio?

## Slide 13
TSI Review & Planning Considerations
Antennas
2 APs
  Wired
  Wireless
Off Ramp Zone Options

## Slide 14
TSI Review & Planning Considerations Ex. 2
Up to 30 high-volume Pods per Radio
Add Omni or Panel Antenna

## Slide 15: Software Programming Computer Set-up

## Slide 16: Software Programming Set-up Tips

## Slide 17: Corridor Considerations NetID / Access Point
Explanation of NetID effects on Access Point Radios
NetID: 1
NetID: 2
NetID: 3
NetID: 4
NetID: 5

## Slide 18: Changes – Requirements & Time Considerations
Reload Config
  System Reboot – loss of detection for minute
  15 minute process (+Pod sync) – constant calls
When Required
  Base Station NetID change
  Access Point replacement
  Access Point Communication change
  Pod replacement
  Pod Add / Delete
  Pod Radio change

## Slide 19
Intersection Design Presence

## Slide 20
Intersection Design Adaptive
Output requirements
Cloning

## Slide 21
Signal Performance Measures
SYSTEM
CONTROL
LOCAL CONTROL
DETECTION
COMMUNICATION

## Slide 22: Detection Requirements SPM
ADVANCE
TURNING MOVEMENT
RED LIGHT MONITOR
STOP BAR

## Slide 23: Detection Requirements (Cont.) SPM
 | Advance Detector | Red Light Monitor (RLM) | Stop bar Detector | Turning Movement Count (TMC)
Approach Delay |  |  |  | 
Approach Volume |  |  |  | 
Arrivals on Red |  |  |  | 
Pedestrian Delay |  |  |  | 
Preemption Details |  |  |  | 
Purdue Coordination Diagram |  |  |  | 
Purdue Phase Termination |  |  |  | 
Purdue Split Failure |  |  |  | 
Split Monitor |  |  |  | 
Turning Movement Counts |  |  |  | 
Yellow and Red Actuations |  |  |  | 

## Slide 24
Intersection Design Example SPM
Minimum Requirements

## Slide 25
Intersection Design Example SPM
Software Design

## Slide 26
New Capabilities
[Preempt] – Flush / Flasher
Speed
Wrong Way Detection

## Slide 27
Reports Available
ATMS Individual Detectors
Volume / Occupancy
Events

## Slide 28: Contact Information
Chris Jannace, Detection Specialist
ChrisJannace@trafficware.com
(O) 281-240-7233 x309
(C) 626-261-0875
Areas of Responsibility:
Louisiana
Mississippi
Texas
Arkansas
Oklahoma
New Mexico
Hawaii